LCLS ‘Q150kG’ LTU QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, December 05, 2007 |
| Work Order/Charge No.: | 9242609 |
| Serial Number: | SLAC – 000366 / SN 009 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU Q150kG QUADS\000366.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on top of magnet where tooling ball sockets are welded to.

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | Cyl. Dia. | X | Y | Z |
| --- | --- | --- | --- | --- |
| Proj. TB 1 | 0.24999 | 2.65296 | 10.21565 | 5.61107 |
| Proj. TB 2 | 0.25000 | 2.65447 | 10.21373 | -5.60579 |
| Proj. TB 3 | 0.25010 | -2.65278 | 10.21438 | -5.60754 |
| Proj. TB 4 | 0.25001 | -2.66054 | 10.21511 | 5.60678 |

Pole Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.25931 | 1.26018 | 0.43250 | 0.43558 | 0.43349 | 0.43289 |
| Upstream End (-Z) | 1.26098 | 1.25998 | 0.43390 | 0.43351 | 0.43338 | 0.43525 |

# Text boxes

+Y

+Z

+Y

+X

+Z

+X