LCLS ‘Q150kG’ LTU QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Thursday, January 17, 2008 |
| Work Order/Charge No.: | 9242609 |
| Serial Number: | SLAC – 000367-010 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU Q150kG QUADS\000367.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on top of magnet where tooling ball sockets are welded to.

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | Form | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| Proj. TB 1 | 0.00019 | 0.25011 | 2.62352 | 10.20889 | 5.60625 | 0.00010 |
| Proj. TB 2 | 0.00019 | 0.24990 | 2.63690 | 10.20569 | -5.59686 | 0.00015 |
| Proj. TB 3 | 0.00011 | 0.24995 | -2.67945 | 10.20133 | -5.60844 | 0.00018 |
| Proj. TB 4 | 0.00078 | 0.24984 | -2.67361 | 10.20447 | 5.60311 | 0.00038 |

.

Pole Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.25997 | 1.25977 | 0.43422 | 0.43477 | 0.42998 | 0.44133 |
| Upstream End (-Z) | 1.25967 | 1.26010 | 0.43298 | 0.43417 | 0.42880 | 0.44020 |

# Text boxes

+Y

+Z

+Y

+X

+Z

+X