LCLS ‘Q150kG’ LTU QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Thursday, January 17, 2008 |
| Work Order/Charge No.: | 9242609 |
| Serial Number: | SLAC – 002600/ SN 008 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU Q150kG QUADS\002600.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on top of magnet where tooling ball sockets are welded to.

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | Form | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| Proj. TB 1 | 0.00012 | 0.24994 | 2.62941 | 10.21758 | 5.60874 | 0.00014 |
| Proj. TB 2 | 0.00009 | 0.24999 | 2.62459 | 10.21296 | -5.60809 | 0.00042 |
| Proj. TB 3 | 0.00007 | 0.24999 | -2.67558 | 10.20643 | -5.61092 | 0.00007 |
| Proj. TB 4 | 0.00011 | 0.24996 | -2.67858 | 10.21112 | 5.60749 | 0.00013 |

.

Pole Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.26021 | 1.26078 | 0.43186 | 0.43504 | 0.43517 | 0.43808 |
| Upstream End (-Z) | 1.26098 | 1.26058 | 0.43122 | 0.43494 | 0.43494 | 0.43718 |

# Text boxes

+Y

+Z

+Y

+X

+Z

+X