LCLS ‘Q150kG’ LTU QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Friday, September 28, 2007 |
| Work Order/Charge No.: | 9242609 |
| Serial Number: | SLAC – 002882 / SN 002 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU Q150kG QUADS\002882.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on top of magnet where tooling ball sockets are welded to.

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Tooling Balls Measured with ½” Tooling Ball Socket

| Tooling Ball | FORM | Sph. Dia. | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00029 | 0.49947 | 2.65778 | 10.20499 | 5.60675 |
| TB 2 | 0.00003 | 0.50006 | 2.65946 | 10.20480 | -5.60851 |
| TB 3 | 0.00031 | 0.49969 | -2.65652 | 10.20455 | -5.60920 |
| TB 4 | 0.00003 | 0.50004 | -2.65666 | 10.20376 | 5.58547 |

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | Cyl. Dia. | X | Y | Z |
| --- | --- | --- | --- | --- |
| Proj. TB 1 | 0.25010 | 2.65854 | 10.20426 | 5.60779 |
| Proj. TB 2 | 0.24987 | 2.65969 | 10.20452 | -5.60885 |
| Proj. TB 3 | 0.25000 | -2.65677 | 10.20405 | -5.60940 |
| Proj. TB 4 | 0.24997 | -2.65577 | 10.20342 | 5.58549 |

.

Pole Data

*Data looking from Downstream End

| Side | Pole Diameter | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.26101 | 1.26122 | 1.26098 | 0.42982 | 0.44535 | 0.42483 | 0.44283 |
| Upstream End (-Z) | 1.25831 | 1.25827 | 1.26088 | 0.42717 | 0.44479 | 0.42486 | 0.44020 |

# Text boxes

+Y

+Z

+Y

+X

+Z

+X