LCLS ‘Q150kG’ LTU QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, January 14, 2008 |
| Work Order/Charge No.: | 9242609 |
| Serial Number: | SLAC – 002884 / SN 013 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU Q150kG QUADS\002884.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on top of magnet where tooling ball sockets are welded to.

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | Form | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| Proj. TB 1 | 0.00015 | 0.24993 | 2.65333 | 10.21230 | 5.60647 | 0.00005 |
| Proj. TB 2 | 0.00010 | 0.24999 | 2.65627 | 10.20818 | -5.60955 | 0.00013 |
| Proj. TB 3 | 0.00007 | 0.25002 | -2.65266 | 10.20664 | -5.61167 | 0.00092 |
| Proj. TB 4 | 0.00014 | 0.25013 | -2.66078 | 10.20919 | 5.60349 | 0.00011 |

.

Pole Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.26146 | 1.25932 | 0.43064 | 0.44007 | 0.43106 | 0.43409 |
| Upstream End (-Z) | 1.26165 | 1.25914 | 0.42998 | 0.44206 | 0.43366 | 0.43733 |

# Text boxes

+Y

+Z

+Y

+X

+Z

+X