LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Friday, February 23, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000218 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000218.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00012 | 0.49933 | 5.00732 | 3.70317 | -8.04452 |
| TB B | 0.00009 | 0.49917 | -1.42857 | 7.31394 | -8.01377 |
| TB C | 0.00018 | 0.49888 | -5.03449 | 3.68246 | -8.02983 |
| TB D | 0.00042 | 0.49923 | -5.25073 | 3.68104 | 6.30315 |
| TB E | 0.00024 | 0.49945 | -1.45980 | 7.31328 | 8.05913 |
| TB F | 0.00019 | 0.49930 | 5.25547 | 3.70312 | 6.29034 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90691 | 0.90682 | 0.00009 |
| B-D | 0.90652 | 0.90663 | 0.00011 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A