LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, March 26, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000223 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000223.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00040 | 0.49670 | 5.03133 | 3.71623 | -8.04045 |
| TB B | 0.00047 | 0.49870 | -1.42063 | 7.31663 | -8.06174 |
| TB C | 0.00019 | 0.49863 | -5.04148 | 3.69048 | -8.08133 |
| TB D | 0.00043 | 0.49867 | -5.28980 | 3.69002 | 6.29343 |
| TB E | 0.00041 | 0.49727 | -1.43417 | 7.31667 | 8.06180 |
| TB F | 0.00055 | 0.49771 | 5.26721 | 3.71589 | 6.29962 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90663 | 0.90697 | 0.00032 |
| B-D | 0.90610 | 0.90569 | 0.00041 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A