LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Friday, March 23, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000238 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000238.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00049 | 0.49742 | 5.02439 | 3.68602 | -8.02600 |
| TB B | 0.00027 | 0.49917 | -1.37446 | 7.31248 | -8.04031 |
| TB C | 0.00029 | 0.49654 | -5.00869 | 3.70381 | -8.04784 |
| TB D | 0.00034 | 0.49719 | -5.19244 | 3.70506 | 6.28542 |
| TB E | 0.00048 | 0.49641 | -1.37494 | 7.31544 | 8.05437 |
| TB F | 0.00047 | 0.49737 | 5.28481 | 3.68511 | 6.31020 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90744 | 0.90775 | 0.00031 |
| B-D | 0.90545 | 0.90622 | 0.00077 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A