LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, February 21, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000269 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000269.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00039 | 0.49690 | 5.04055 | 3.69963 | -8.04079 |
| TB B | 0.00008 | 0.49794 | -1.40055 | 7.31459 | -8.04370 |
| TB C | 0.00008 | 0.49935 | -5.02864 | 3.70890 | -8.04076 |
| TB D | 0.00046 | 0.49692 | -5.28813 | 3.70528 | 6.29310 |
| TB E | 0.00024 | 0.49831 | -1.40888 | 7.30934 | 8.05351 |
| TB F | 0.00021 | 0.49806 | 5.28575 | 3.69809 | 6.29598 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90917 | 0.90490 | 0.00427 |
| B-D | 0.90980 | 0.90557 | 0.00423 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A