LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, March 26, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000305 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000305.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00048 | 0.49660 | 5.04721 | 3.70047 | -8.03672 |
| TB B | 0.00020 | 0.49770 | -1.38658 | 7.31919 | -8.02645 |
| TB C | 0.00057 | 0.49739 | -5.01452 | 3.70411 | -8.02948 |
| TB D | 0.00007 | 0.49669 | -5.23398 | 3.70486 | 6.28162 |
| TB E | 0.00042 | 0.49688 | -1.40919 | 7.32016 | 8.07233 |
| TB F | 0.00047 | 0.49614 | 5.26652 | 3.70107 | 6.29811 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90660 | 0.90419 | 0.00241 |
| B-D | 0.90643 | 0.90653 | 0.00010 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A