LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, February 27, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000307 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000307.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00009 | 0.49961 | 4.99935 | 3.68876 | -8.02399 |
| TB B | 0.00016 | 0.49871 | -1.38033 | 7.31820 | -8.01561 |
| TB C | 0.00033 | 0.49710 | -4.98823 | 3.68789 | -7.99925 |
| TB D | 0.00014 | 0.49979 | -5.22091 | 3.68710 | 6.28801 |
| TB E | 0.00027 | 0.49732 | -1.35342 | 7.31943 | 8.00644 |
| TB F | 0.00003 | 0.49974 | 5.24865 | 3.69258 | 6.29752 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.91084 | 0.90455 | 0.00629 |
| B-D | 0.90625 | 0.90622 | 0.00003 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A