LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, January 17, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000308 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000308.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00035 | 0.49772 | 5.06479 | 3.69378 | -8.06684 |
| TB B | 0.00036 | 0.49800 | -1.40078 | 7.31585 | -8.03895 |
| TB C | 0.00015 | 0.49937 | -4.94032 | 3.70779 | -7.98910 |
| TB D | 0.00037 | 0.49784 | -5.24134 | 3.70807 | 6.27821 |
| TB E | 0.00041 | 0.49810 | -1.39636 | 7.31511 | 8.05735 |
| TB F | 0.00035 | 0.49792 | 5.24986 | 3.69484 | 6.26869 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90697 | 0.90756 | 0.00059 |
| B-D | 0.90685 | 0.90618 | 0.00067 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A