LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, February 21, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000304 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000304.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00006 | 0.49913 | 5.00712 | 3.70673 | -8.03280 |
| TB B | 0.00003 | 0.49967 | -1.40711 | 7.32741 | -8.02921 |
| TB C | 0.00012 | 0.49840 | -4.95756 | 3.67656 | -8.02702 |
| TB D | 0.00024 | 0.49740 | -5.29555 | 3.67526 | 6.28779 |
| TB E | 0.00023 | 0.49766 | -1.41054 | 7.32776 | 8.02866 |
| TB F | 0.00002 | 0.49982 | 5.21845 | 3.70606 | 6.27925 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90691 | 0.90712 | 0.00021 |
| B-D | 0.90654 | 0.90662 | 0.00008 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A