LCLS ‘0.91Q17.72’ LTU Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Thursday, March 01, 2007 |
| Work Order/Charge No.: | 21699-1 |
| Serial Number: | 000322 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS LTU QUAD\000322.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Clocking plane where TB A,C, D, & E reside.

“Z” Zero

- Mid-plane of the magnet (pole planes on each end).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00032 | 0.49766 | 5.02721 | 3.70244 | -8.04899 |
| TB B | 0.00004 | 0.49883 | -1.42687 | 7.32835 | -8.06191 |
| TB C | 0.00007 | 0.49849 | -5.05671 | 3.70402 | -8.05395 |
| TB D | 0.00028 | 0.49937 | -5.24656 | 3.70324 | 6.31254 |
| TB E | 0.00015 | 0.49840 | -1.39451 | 7.32800 | 8.11396 |
| TB F | 0.00029 | 0.49717 | 5.25541 | 3.70221 | 6.28085 |

.

Pole Distances

| Pole | -Z side | +Z side |  |
| --- | --- | --- | --- |
| A-C | 0.90633 | 0.90575 | 0.00058 |
| B-D | 0.90689 | 0.90698 | 0.00009 |

# Text boxes

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A