LCLS ‘QE’ QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, November 27, 2006 |
| Work Order/Charge No.: | 92-4264-2 |
| Serial Number: | 000016 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS QE QUAD'S\000016.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- A 4 point plane on the top of where 2 arrows indicate in the picture below.

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- Geometric Axis of the Poles of the magnet.

| Side View | Front View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00080 | 0.49254 | 8.22814 | 1.18355 | 1.75159 |
| TB 2 | 0.00006 | 0.50006 | 8.23325 | 1.14889 | -1.30819 |
| TB 3 | 0.00005 | 0.50001 | 1.13435 | 8.24412 | 1.71933 |
| TB 4 | 0.00003 | 0.50003 | 1.16048 | 8.25551 | -1.30231 |
| TB 5 | 0.00009 | 0.49987 | -8.24721 | 1.15478 | 1.74813 |
| TB 6 | 0.00007 | 0.49986 | -8.23914 | 1.14125 | -1.33868 |

Pole Distances

| Pole | +Z side | -Z side |  |
| --- | --- | --- | --- |
| A-C | 1.08821 | 1.08954 | 0.00133 |
| B-D | 1.08457 | 1.08955 | 0.00498 |

*** Points collected approx. 0.125 from each end

*** Picture to the left is looking down from +Z

# Text boxes

TB 6

TB 5

TB 2

TB 1

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A