LCLS ‘QE’ QUADRUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Friday, October 26, 2007 |
| Work Order/Charge No.: | 23188-49 |
| Serial Number: | 002799 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS QE QUAD'S\002799.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- A 4 point plane on the top of where 2 arrows indicate in the picture below.

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- Geometric Axis of the Poles of the magnet.

| Side View | Front View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00004 | 0.49933 | 8.25153 | 1.21983 | 1.72053 |
| TB 2 | 0.00016 | 0.49893 | 8.25326 | 1.21045 | -1.25385 |
| TB 3 | 0.00028 | 0.49810 | 1.22394 | 8.27396 | 1.70571 |
| TB 4 | 0.00025 | 0.49915 | 1.21396 | 8.25929 | -1.28178 |
| TB 5 | 0.00021 | 0.49871 | -8.25228 | 1.21428 | 1.72982 |
| TB 6 | 0.00015 | 0.49923 | -8.24934 | 1.21164 | -1.25123 |

Pole Distances

| Pole | +Z side | -Z side |  |
| --- | --- | --- | --- |
| A-C | 1.08513 | 1.08695 | 0.00182 |
| B-D | 1.08477 | 1.08751 | 0.00274 |

*** Points collected approx. 0.125 from each end

*** Picture to the left is looking down from +Z

# Text boxes

TB 6

TB 5

TB 2

TB 1

+Y

+Z

+Y

+X

+X

+Z

D

C

B

A