LCLS Injector Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Tuesday, July 11, 2006 |
| Work Order/Charge No.: | 92-4215-8 |
| Serial Number | 000421 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet

Spatial Alignment

- A line on the top part of the magnet

  - +X goes towards (Magnet Info Label)

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00038 | 0.49838 | 6.50042 | 8.87837 | -1.24980 |
| TB 2 | 0.00077 | 0.49579 | -6.49856 | 8.88044 | -1.24986 |
| TB 3 | 0.00014 | 0.49883 | -6.49769 | 8.87965 | 1.25049 |
| TB 4 | 0.00111 | 0.49741 | 6.50087 | 8.87896 | 1.24814 |

Additional Requested Measurements

Tangent Point Straightness

- 0.00034

- 0.00025

- 0.00019

- 0.00058

Parallelism to Beamline

- 0.00031

- 0.00032

- 0.00026

- 0.00065

Distance of opposite Tangent

Axis

A-C = 1.25975 (0.62989, 0.62987)

B-D = 1.25896 (0.62964, 0.62932)

# Text boxes

TB 1

TB 2

TB 3

TB 4

Z+

+Z

+X

A

B

C

D

View From +Z