LCLS Injector Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Tuesday, July 11, 2006 |
| Work Order/Charge No.: | 92-4215-8 |
| Serial Number | 000425 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet

Spatial Alignment

- A line on the top part of the magnet

  - +X goes towards (Magnet Info Label)

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00086 | 0.49725 | 6.49968 | 8.87717 | -1.25176 |
| TB 2 | 0.00048 | 0.49751 | -6.49867 | 8.87643 | -1.24975 |
| TB 3 | 0.00022 | 0.49844 | -6.49887 | 8.87722 | 1.24993 |
| TB 4 | 0.00053 | 0.49781 | 6.50011 | 8.87772 | 1.24805 |

Additional Requested Measurements

Tangent Point Straightness

- 0.00047

- 0.00018

- 0.00020

- 0.00030

Parallelism to Beamline

- 0.00046

- 0.00020

- 0.00023

- 0.00029

Distance of opposite Tangent

Axis

A-C = 1.25981 (0.62994, 0.62987)

B-D = 1.25974 (0.62983, 0.62990)

# Text boxes

TB 1

TB 2

TB 3

TB 4

Z+

+Z

+X

A

B

C

D

View From +Z