LCLS Injector Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Tuesday, July 11, 2006 |
| Work Order/Charge No.: | 92-4215-8 |
| Serial Number | 000427 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet

Spatial Alignment

- A line on the top part of the magnet

  - +X goes towards (Magnet Info Label)

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00100 | 0.49517 | 6.49797 | 8.88086 | -1.24932 |
| TB 2 | 0.00101 | 0.49524 | -6.50078 | 8.87729 | -1.24961 |
| TB 3 | 0.00107 | 0.49450 | -6.50211 | 8.87781 | 1.25051 |
| TB 4 | 0.00072 | 0.49592 | 6.49686 | 8.88091 | 1.25152 |

Additional Requested Measurements

Tangent Point Straightness

- 0.00013

- 0.00006

- 0.00023

- 0.00025

Parallelism to Beamline

- 0.00007

- 0.00022

- 0.00021

- 0.00030

Distance of opposite Tangent

Axis

A-C = 1.26001 (0.63001, 0.62999)

B-D = 1.25901 (0.62951, 0.62950)

# Text boxes

TB 1

TB 2

TB 3

TB 4

Z+

+Z

+X

A

B

C

D

View From +Z