LCLS LE 3.25Q20 Quadrupole (from PEP II)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Friday, July 21, 2006 |
| Work Order/Charge No.: | 92-4261-0 |
| Serial Number | 001 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet (Outer Most Planes)

Spatial Alignment

- A line on the top part of the magnet

  - +X goes opposite stamped SA-344-913-01

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y” (see photographs for more clarity above)

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00156 | 0.49182 | 6.50166 | 8.88043 | -1.24926 |
| TB 2 | 0.00074 | 0.49528 | -6.49888 | 8.87853 | -1.24818 |
| TB 3 | 0.00049 | 0.49705 | -6.49947 | 8.87789 | 1.25166 |
| TB 4 | 0.00070 | 0.49624 | 6.49945 | 8.87898 | 1.25094 |

Additional Requested Measurements

Pole Tip Dist A-C Z+= 3.25129

Pole Tip Dist A-C Z-= 3.25383

Pole Tip Dist B-D Z+= 3.25336

Pole Tip Dist B-D Z-= 3.25155

Z+ Side = 0.0021

Z- Side = 0.0023

Along A-C = 0.0025 small to big from positive to negative “Z”

Along B-D = 0.0018 small to big from negative to positive “Z”

(rises in opposite directions).

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

A

B

C

D

View From +Z

Y+

Y+

X+