PEP II QDMP#1 Quadrupole Refurbishment

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Wednesday, August 09, 2006 |
| Work Order/Charge No.: | 92-4261-0 |
| Serial Number | QDMP#1 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet (Outer Most Planes)

Spatial Alignment

- A line on the top part of the magnet

  - +X goes opposite stamped SA-344-913-01

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y” (see photographs for more clarity above)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00065 | 0.49778 | 6.37708 | 4.86134 | -7.88055 |
| TB 2 | 0.00045 | 0.49663 | -6.35666 | 4.88955 | -8.00748 |
| TB 3 | 0.00039 | 0.49763 | -6.36165 | 4.89092 | 11.00850 |
| TB 4 | 0.00037 | 0.49660 | 6.35963 | 4.85991 | 11.00168 |
| TB 5 | 0.00038 | 0.49777 | 0.00337 | 8.30121 | 11.04370 |
| TB 6 | 0.00018 | 0.49894 | -0.00057 | 8.30042 | -8.01525 |

Additional Requested Measurements

Pole Tip Dist A-C Z+= 3.24986

Pole Tip Dist A-C Z-= 3.25075

Pole Tip Dist B-D Z+= 3.25093

Pole Tip Dist B-D Z-= 3.25250

Z+ Side = 0.0011

Z- Side = 0.0017

Along A-C = -0.0009 +Z to -Z

Along B-D = -0.0015 + Z to -Z

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

View From +Z

Y+

Y+

X+

TB 6

TB 5