PEP II QDMP#4 Quadrupole Refurbishment

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Monday, August 14, 2006 |
| Work Order/Charge No.: | 92-4261-0 |
| Serial Number | QDMP#4 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet (Outer Most Planes)

Spatial Alignment

- A line on the top part of the magnet

  - +X goes opposite stamped SA-344-913-01

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y” (see photographs for more clarity above)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00083 | 0.49668 | 6.37042 | 4.92563 | -8.02760 |
| TB 2 | 0.00026 | 0.49644 | -6.39024 | 4.86700 | -7.99370 |
| TB 3 | 0.00054 | 0.49641 | -6.36234 | 4.87806 | 11.00191 |
| TB 4 | 0.00058 | 0.49660 | 6.33300 | 4.90414 | 10.98720 |
| TB 5 | 0.00032 | 0.49866 | 0.01049 | 8.29882 | 11.04973 |
| TB 6 | 0.00039 | 0.49742 | -0.03169 | 8.30375 | -8.02732 |

Additional Requested Measurements

Pole Tip Dist A-C Z+= 3.25581

Pole Tip Dist A-C Z-= 3.25014

Pole Tip Dist B-D Z+= 3.25640

Pole Tip Dist B-D Z-= 3.25338

Z+ Side = 0.0006

Z- Side = 0.0032

Along A-C = +0.0057 +Z to -Z

Along B-D = +0.0030 + Z to -Z

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

View From +Z

Y+

Y+

X+

TB 6

TB 5