PEP II QDMP#2 Quadrupole Refurbishment

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Monday, August 14, 2006 Revised Tuesday, September 30, 2008 |
| Work Order/Charge No.: | 92-4261-0 |
| Serial Number | QDMP#2 |
| LCLS BARCODE | 002417 |
| URL | http://www-group\met\Quality\FIDUCIAL REPORTS\LCLS REFURBISH\QDMP2.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the Pole Faces.

Spatial Alignment

- A line on the top part of the magnet

  - +X goes opposite stamped SA-344-913-01

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y” (see photographs for more clarity above)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00083 | 0.49670 | 6.41800 | 4.88796 | -9.55720 |
| TB 2 | 0.00050 | 0.49729 | -6.32473 | 4.87592 | -9.37007 |
| TB 3 | 0.00064 | 0.49633 | -6.35617 | 4.89499 | 9.55274 |
| TB 4 | 0.00020 | 0.49966 | 6.34046 | 4.87925 | 9.54814 |
| TB 5 | 0.00047 | 0.49684 | 0.00385 | 8.31000 | 9.56889 |
| TB 6 | 0.00066 | 0.49629 | -0.03398 | 8.31714 | -9.53440 |

Additional Requested Measurements

Pole Tip Dist A-C Z+= 3.25189

Pole Tip Dist A-C Z-= 3.25575

Pole Tip Dist B-D Z+= 3.24738

Pole Tip Dist B-D Z-= 3.25486

Z+ Side = 0.0045

Z- Side = 0.0009

Along A-C = -0.0039 +Z to -Z

Along B-D = -0.0074 + Z to -Z

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

View From +Z

Y+

Y+

X+

TB 6

TB 5