PEP II QDMP#3 Quadrupole Refurbishment

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Thursday, August 03, 2006 Revised Tuesday, September 30, 2008 |
| Work Order/Charge No.: | 92-4261-0 |
| Serial Number | QDMP#3 |
| LCLS BARCODE | 002415 |
| URL | http://www-group\met\Quality\FIDUCIAL REPORTS\LCLS REFURBISH\QDMP3.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the Pole Faces.

Spatial Alignment

- A line on the top part of the magnet

  - +X goes opposite stamped SA-344-913-01

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y” (see photographs for more clarity above)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00082 | 0.49629 | 6.40353 | 4.87561 | -9.54392 |
| TB 2 | 0.00072 | 0.49613 | -6.32486 | 4.88229 | -9.57312 |
| TB 3 | 0.00055 | 0.49641 | -6.39686 | 4.89378 | 9.55756 |
| TB 4 | 0.00080 | 0.49759 | 6.36654 | 4.87008 | 9.56918 |
| TB 5 | 0.00061 | 0.49692 | 0.04368 | 8.31086 | 9.54508 |
| TB 6 | 0.00047 | 0.49756 | 0.00749 | 8.31190 | -9.52832 |

Additional Requested Measurements

Pole Tip Dist A-C Z+= 3.25114

Pole Tip Dist A-C Z-= 3.25320

Pole Tip Dist B-D Z+= 3.25331

Pole Tip Dist B-D Z-= 3.25100

Z+ Side = 0.0021

Z- Side = 0.0023

Along A-C = 0.0022 small to big from positive to negative “Z”

Along B-D = 0.0022 small to big from negative to positive “Z”

(rises in opposite directions).

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

A

B

C

D

View From +Z

Y+

Y+

X+

TB 6

TB 5