PEP II QDMP#5 Quadrupole Refurbishment

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Friday, August 04, 2006 Revised Tuesday, September 30, 2008 |
| Work Order/Charge No.: | 92-4261-0 |
| Serial Number | QDMP#5 |
| LCLS BARCODE |  |
| URL | http://www-group\met\Quality\FIDUCIAL REPORTS\LCLS REFURBISH\QDMP5.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the Pole Faces.

Spatial Alignment

- A line on the top part of the magnet

  - +X goes opposite stamped SA-344-913-01

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y” (see photographs for more clarity above)

| Tooling Ball | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00035 | 0.49834 | 6.38277 | 4.87717 | -9.37051 |
| TB 2 | 0.00054 | 0.49769 | -6.38634 | 4.88180 | -9.26792 |
| TB 3 | 0.00044 | 0.49703 | -6.34164 | 4.88806 | 9.39214 |
| TB 4 | 0.00042 | 0.49832 | 6.42008 | 4.86978 | 9.39105 |
| TB 5 | 0.00010 | 0.49926 | 0.01933 | 8.30154 | 9.55290 |
| TB 6 | 0.00054 | 0.49701 | -0.03646 | 8.30244 | -9.90404 |

Additional Requested Measurements

Pole Tip Dist A-C Z+= 3.24891

Pole Tip Dist A-C Z-= 3.25628

Pole Tip Dist B-D Z+= 3.25133

Pole Tip Dist B-D Z-= 3.25087

Z+ Side = 0.0024

Z- Side = 0.0054

Along A-C = 0.0074 +Z to -Z

Along B-D = 0.0005 small to big from negative to positive “Z”

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

A

B

C

D

View From +Z

Y+

Y+

X+

TB 6

TB 5