LCLS SINGLE BEAM DUMP (SBD/TDKIK)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | E. Bong |
| Date: | Thursday, November 06, 2008 |
| Work Order/Charge No.: | 23755-10 |
| Serial Number: | 001 or TDKIK |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS SBD\SBD TDKIK.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane measurement on top of  2x Stainless Steel End Block.

- Sets orientation in +Y

Spatial Alignment

- On inside of core, 2 circles center points create the beam line axis, +Z, sets zero in X/Y.

“Z” Zero

- Mid-Plane of the part measuring the 2 End Blocks surface.

| View from +Z | View from +X |
| --- | --- |

Tooling Ball Measurements/Locations

** Used ½” Tooling Ball Diameter with 1” offset from Ball Center.

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00056 | 0.49780 | -4.05701 | 6.49874 | 10.75203 |
| TB 2 | 0.00064 | 0.49610 | 4.00389 | 6.51018 | 10.74335 |
| TB 3 | 0.00050 | 0.49730 | 0.03969 | 6.48131 | -11.26080 |

# Text boxes

+X

+X

TB 3

+Z

TB 2

TB 1

+X

+Z

+Y

+Y

+Z

+X