LCLS Tweeter Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, August 09, 2006 |
| Work Order/Charge No.: | 92-4261-3 |
| Serial Number: | 001028 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS TWEETER QUADS\TWEETER QUAD 3.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet

Spatial Alignment

- A plane on the top part of the magnet (red) by the Tooling Ball Sockets.

  - +X is from TB 3 & 4 side to TB 1 & 2 side.

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- On both ends

  - Tangent point of each radii (4 on each end, 8 total).

    - Create a line between diagonal tangent points creates 2 lines.

      - Intersect the lines.

        - Creates a point on each end.

- Create a line of these 2 end points

  - This is the “X” & “Y” Zero, and Beamline or” Z” Axis.

| ISO | Front View |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00059 | 0.49663 | 1.96530 | 6.74297 | 1.25419 |
| TB 2 | 0.00094 | 0.49628 | 1.96462 | 6.74048 | -1.25456 |
| TB 3 | 0.00026 | 0.49854 | -1.96905 | 6.73949 | -1.25252 |
| TB 4 | 0.00062 | 0.49664 | -1.97091 | 6.74026 | 1.26004 |

Pole Distances

| Pole | +Z side | -Z side |  |
| --- | --- | --- | --- |
| A-C | 1.69097 | 1.69067 | 0.00030 |
| B-D | 1.69151 | 1.69206 | 0.00055 |

# Text boxes

+Y

-Z

+Y

+X

+X

+Z

A

B

C

D