LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, May 30, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000707 / STAMPED – 24 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000707.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00014 | 0.24997 | 3.36974 | 6.81319 | 1.50890 | 0.00007 |
| TB 2 | 0.00125 | 0.24980 | -3.37905 | 6.81107 | 1.50380 | 0.00066 |
| TB 3 | 0.00015 | 0.25003 | -3.37910 | 6.81243 | -1.49503 | 0.00031 |
| TB 4 | 0.00014 | 0.25009 | 3.37157 | 6.81363 | -1.48981 | 0.00007 |
| TB 5 | 0.00008 | 0.24997 | 6.57538 | 0.13546 | 0.00215 | 0.00015 |

Z-distance of Quad = 3.59612

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43270 | 0.43202 | 0.15861 | 0.15892 | 0.15973 | 0.16054 |
| Upstream End (-Z) | 0.43260 | 0.43201 | 0.15944 | 0.15977 | 0.15858 | 0.15934 |

| Side | A-Rad | B-Rad | C-Rad | D-Rad |
| --- | --- | --- | --- | --- |
| +Z | 0.21662 | 0.21607 | 0.21609 | 0.21595 |
| -Z | 0.21661 | 0.21597 | 0.21600 | 0.21605 |

| Side | J | K | L | M | N | O | P | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| +Z | 0.07965 | 0.07995 | 0.08059 | 0.07978 | 0.07883 | 0.08012 | 0.07881 | 0.08008 |
| -Z | 0.08069 | 0.07972 | 0.07963 | 0.08001 | 0.07943 | 0.07953 | 0.08024 | 0.07789 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X