LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, May 30, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000709 / STAMPED – 30 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000709.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00017 | 0.25007 | 3.37386 | 6.81270 | 1.48710 | 0.00006 |
| TB 2 | 0.00014 | 0.24997 | -3.37810 | 6.81135 | 1.49752 | 0.00013 |
| TB 3 | 0.00020 | 0.24994 | -3.38199 | 6.81159 | -1.50183 | 0.00014 |
| TB 4 | 0.00017 | 0.24999 | 3.36676 | 6.81412 | -1.51109 | 0.00011 |
| TB 5 | 0.00012 | 0.25018 | 6.57718 | .13657 | 0.00364 | 0.00008 |

Z-distance of Quad = 3.59542

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43610 | 0.43164 | 0.16057 | 0.15880 | 0.16086 | 0.15785 |
| Upstream End (-Z) | 0.43275 | 0.43294 | 0.15510 | 0.16264 | 0.15797 | 0.16165 |

| Side | A-Rad | B-Rad | C-Rad | D-Rad |
| --- | --- | --- | --- | --- |
| +Z | 0.22022 | 0.21583 | 0.21592 | 0.21580 |
| -Z | 0.21634 | 0.21657 | 0.21642 | 0.21638 |

| Side | J | K | L | M | N | O | P | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| +Z | 0.08054 | 0.07997 | 0.07787 | 0.07945 | 0.08112 | 0.08080 | 0.07800 | 0.08032 |
| -Z | 0.07887 | 0.07997 | 0.08168 | 0.07620 | 0.07890 | 0.08084 | 0.08180 | 0.07909 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X