LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, April 25, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000710 / STAMPED – 10 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000710.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00012 | 0.24988 | 3.36691 | 6.81428 | 1.49900 | 0.00009 |
| TB 2 | 0.00014 | 0.24999 | -3.38133 | 6.81391 | 1.48857 | 0.00007 |
| TB 3 | 0.00015 | 0.24993 | -3.37393 | 6.81436 | -1.51088 | 0.00008 |
| TB 4 | 0.00016 | 0.25000 | 3.37536 | 6.81348 | -1.49976 | 0.00006 |
| TB 5 | 0.00010 | 0.25012 | 6.57897 | 0.13560 | 0.00131 | 0.00010 |

Z-distance of Quad = 3.58365

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43487 | 0.43242 | 0.15866 | 0.15993 | 0.15922 | 0.16073 |
| Upstream End (-Z) | 0.43283 | 0.43393 | 0.15590 | 0.15997 | 0.15922 | 0.16088 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X