LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Thursday, April 24, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000712 / STAMPED – 13 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000712.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00015 | 0.25009 | 3.37558 | 6.81122 | 1.49101 | 0.00010 |
| TB 2 | 0.00015 | 0.25006 | -3.37475 | 6.81549 | 1.49565 | 0.00005 |
| TB 3 | 0.00011 | 0.25014 | -3.37436 | 6.81680 | -1.50333 | 0.00009 |
| TB 4 | 0.00011 | 0.25009 | 3.37740 | 6.81012 | -1.51012 | 0.00010 |
| TB 5 | 0.00008 | 0.25004 | 6.57688 | 0.13026 | 0.00203 | 0.00010 |

Z-distance of Quad = 3.59098

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43350 | 0.43317 | 0.15901 | 0.15838 | 0.15613 | 0.15974 |
| Upstream End (-Z) | 0.43484 | 0.43410 | 0.15854 | 0.15874 | 0.15737 | 0.16194 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X