LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Wednesday, April 23, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000713 / STAMPED – 34 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000713.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00014 | 0.25012 | 3.36692 | 6.81879 | 1.49828 | 0.00017 |
| TB 2 | 0.00010 | 0.25001 | -3.38326 | 6.81452 | 1.49043 | 0.00008 |
| TB 3 | 0.00015 | 0.25004 | -3.38231 | 6.81185 | -1.50710 | 0.00012 |
| TB 4 | 0.00051 | 0.25002 | 3.36945 | 6.81320 | -1.50258 | 0.00025 |
| TB 5 | 0.00013 | 0.25005 | 6.57542 | 0.14065 | 0.01458 | 0.00017 |

Z-distance of Quad = 3.60066

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43271 | 0.43409 | 0.16570 | 0.15940 | 0.16455 | 0.15624 |
| Upstream End (-Z) | 0.43445 | 0.43424 | 0.16479 | 0.16076 | 0.15626 | 0.16325 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X