LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, April 25, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000714 / STAMPED – 04 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000714.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00014 | 0.24997 | 3.37308 | 6.81809 | 1.47981 | 0.00017 |
| TB 2 | 0.00011 | 0.25002 | -3.37641 | 6.81000 | 1.49557 | 0.000013 |
| TB 3 | 0.00013 | 0.24995 | -3.38039 | 6.80776 | -1.50397 | 0.00063 |
| TB 4 | 0.00009 | 0.25009 | 3.36367 | 6.81578 | -1.51676 | 0.00006 |
| TB 5 | 0.00010 | 0.25011 | 6.58427 | 0.14406 | -0.00809 | 0.00012 |

Z-distance of Quad = 3.58642

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43490 | 0.43343 | 0.16077 | 0.16056 | 0.16023 | 0.15789 |
| Upstream End (-Z) | 0.43588 | 0.43131 | 0.15840 | 0.15958 | 0.16024 | 0.15761 |

| Side | A-Rad | B-Rad | C-Rad | D-Rad |
| --- | --- | --- | --- | --- |
| +Z | 0.21665 | 0.21667 | 0.21828 | 0.21677 |
| -Z | 0.22013 | 0.21563 | 0.21575 | 0.21570 |

| Side | J | K | L | M | N | O | P | Q |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| +Z | 0.08168 | 0.08016 | -0.07774 | 0.08153 | -0.07924 | -0.07914 | 0.08142 | -0.07855 |
| -Z | 0.07873 | 0.07932 | -0.07829 | 0.07811 | -0.08028 | -0.08296 | 0.07662 | 0.08151 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X