LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Wednesday, April 23, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000715 / STAMPED – 33 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000715.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00052 | 0.24988 | 3.37066 | 6.81266 | 1.50410 | 0.00012 |
| TB 2 | 0.00054 | 0.24984 | -3.37765 | 6.81198 | 1.49086 | 0.00007 |
| TB 3 | 0.00056 | 0.24980 | -3.37262 | 6.81384 | -1.50842 | 0.00012 |
| TB 4 | 0.00052 | 0.24994 | 3.37479 | 6.81489 | -1.49232 | 0.00006 |
| TB 5 | 0.00016 | 0.25001 | 6.58130 | 0.14069 | 0.00181 | 0.00015 |

Z-distance of Quad = 3.61139

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43560 | 0.43166 | 0.16137 | 0.15601 | 0.16288 | 0.15903 |
| Upstream End (-Z) | 0.43321 | 0.43503 | 0.15752 | 0.16442 | 0.15778 | 0.16180 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X