LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Monday, March 24, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000717 / STAMPED – 17 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000717.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00011 | 0.25002 | 3.36317 | 6.81276 | 1.49470 | 0.00011 |
| TB 2 | 0.00020 | 0.24995 | -3.38615 | 6.81146 | 1.50349 | 0.00016 |
| TB 3 | 0.00013 | 0.25010 | -3.38260 | 6.81261 | -1.49759 | 0.00027 |
| TB 4 | 0.00013 | 0.24989 | 3.36363 | 6.81168 | -1.50640 | 0.00019 |
| TB 5 | 0.00009 | 0.25007 | 6.57695 | 0.13610 | 0.01600 | 0.00021 |

Z-distance of Quad = 3.59585

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43313 | 0.43296 | 0.15938 | 0.15786 | 0.16016 | 0.16039 |
| Upstream End (-Z) | 0.43373 | 0.43257 | 0.16083 | 0.16038 | 0.15814 | 0.16025 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X