LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Tuesday, April 22, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000718 / STAMPED – 31 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000718.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00022 | 0.24997 | 3.37996 | 6.81260 | 1.50998 | 0.00013 |
| TB 2 | 0.00016 | 0.24995 | -3.36839 | 6.81527 | 1.51123 | 0.00014 |
| TB 3 | 0.00012 | 0.25006 | -3.36990 | 6.81601 | -1.48724 | 0.00018 |
| TB 4 | 0.00013 | 0.25001 | 3.37943 | 6.81347 | -1.48864 | 0.00030 |
| TB 5 | 0.00015 | 0.25017 | 6.58208 | 0.13855 | 0.01404 | 0.00027 |

Z-distance of Quad = 3.59569

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43426 | 0.43225 | 0.15777 | 0.16102 | 0.15791 | 0.16124 |
| Upstream End (-Z) | 0.43339 | 0.43228 | 0.15693 | 0.16095 | 0.16247 | 0.15861 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X