LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Tuesday, April 22, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000719 / STAMPED – 36 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000719.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00021 | 0.24982 | 3.37892 | 6.81414 | 1.49266 | 0.00021 |
| TB 2 | 0.00023 | 0.24995 | -3.37216 | 6.81361 | 1.51260 | 0.00022 |
| TB 3 | 0.00016 | 0.24993 | -3.37964 | 6.81572 | -1.48822 | 0.00009 |
| TB 4 | 0.00020 | 0.24992 | 3.37299 | 6.81331 | -1.50790 | 0.00010 |
| TB 5 | 0.00008 | 0.25008 | 6.57844 | 0.13233 | -0.00644 | 0.00009 |

Z-distance of Quad = 3.58683

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43377 | 0.43198 | 0.15992 | 0.15919 | 0.16321 | 0.15903 |
| Upstream End (-Z) | 0.43335 | 0.43311 | 0.16035 | 0.16152 | 0.15641 | 0.16034 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X