LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Monday, April 21, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000720 / STAMPED – 01 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000720.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00011 | 0.25001 | 3.37200 | 6.81176 | 1.49929 | 0.00007 |
| TB 2 | 0.00014 | 0.24990 | -3.37483 | 6.81086 | 1.50336 | 0.00005 |
| TB 3 | 0.00010 | 0.24996 | -3.37789 | 6.81240 | -1.49495 | 0.00015 |
| TB 4 | 0.00008 | 0.24999 | 3.36969 | 6.81154 | -1.49839 | 0.00009 |
| TB 5 | 0.00004 | 0.25005 | 6.57745 | 0.13894 | 0.00684 | 0.00009 |

Z-distance of Quad = 3.57795

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43327 | 0.43271 | 0.15981 | 0.15983 | 0.15914 | 0.15893 |
| Upstream End (-Z) | 0.43314 | 0.43469 | 0.15746 | 0.16247 | 0.15767 | 0.16200 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X