LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Wednesday, March 21, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000721 / STAMPED – 18 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000721.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00008 | 0.24992 | 3.36475 | 6.81384 | 1.50205 | 0.00016 |
| TB 2 | 0.00014 | 0.24991 | -3.38002 | 6.81170 | 1.50498 | 0.00011 |
| TB 3 | 0.00015 | 0.24999 | -3.37784 | 6.81181 | -1.49896 | 0.00012 |
| TB 4 | 0.00013 | 0.24991 | 3.36908 | 6.81287 | -1.50038 | 0.00014 |
| TB 5 | 0.00008 | 0.25003 | 6.57954 | 0.13605 | 0.00352 | 0.00010 |

Z-distance of Quad = 3.59720

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43450 | 0.43188 | 0.16037 | 0.15879 | 0.16164 | 0.15914 |
| Upstream End (-Z) | 0.43349 | 0.43343 | 0.16059 | 0.16117 | 0.15816 | 0.16198 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X