LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Wednesday, March 21, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000722 / STAMPED – 21 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000722.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00012 | 0.25000 | 3.37729 | 6.81295 | 1.50179 | 0.00010 |
| TB 2 | 0.00011 | 0.25001 | -3.37236 | 6.81305 | 1.50429 | 0.00039 |
| TB 3 | 0.00010 | 0.25015 | -3.371 | 6.81330 | -1.49376 | 0.00022 |
| TB 4 | 0.00012 | 0.25008 | 3.37623 | 6.81238 | -1.49945 | 0.00032 |
| TB 5 | 0.00013 | 0.25003 | 6.57896 | 0.13255 | 0.00890 | 0.00033 |

Z-distance of Quad = 3.59473

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43219 | 0.43446 | 0.16022 | 0.16079 | 0.15952 | 0.15950 |
| Upstream End (-Z) | 0.43114 | 0.43506 | 0.16046 | 0.15839 | 0.15927 | 0.16079 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X