LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Thursday, March 20, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000724 / STAMPED – 20 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000724.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00012 | 0.24997 | 3.36363 | 6.81416 | 1.50264 | 0.00041 |
| TB 2 | 0.00011 | 0.25003 | -3.38739 | 6.81089 | 1.46895 | 0.00008 |
| TB 3 | 0.00036 | 0.25012 | -3.37155 | 6.81102 | -1.52899 | 0.00010 |
| TB 4 | 0.00014 | 0.25014 | 3.37844 | 6.81265 | -1.49675 | 0.00004 |
| TB 5 | 0.00011 | 0.25005 | 6.57674 | 0.13463 | -0.00095 | 0.00013 |

Z-distance of Quad = 3.57352

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43332 | 0.43329 | 0.16169 | 0.16022 | 0.15819 | 0.15645 |
| Upstream End (-Z) | 0.43236 | 0.43322 | 0.15910 | 0.16024 | 0.15894 | 0.16131 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X