LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Wednesday, March 21, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000725 / STAMPED – 22 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000725.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00013 | 0.25001 | 3.38498 | 6.81133 | 1.50009 | 0.00020 |
| TB 2 | 0.00009 | 0.25014 | -3.36924 | 6.81382 | 1.50400 | 0.00009 |
| TB 3 | 0.00013 | 0.25002 | -3.36743 | 6.81566 | -1.49603 | 0.00016 |
| TB 4 | 0.00009 | 0.25002 | 3.38111 | 6.80903 | -1.49943 | 0.00004 |
| TB 5 | 0.00014 | 0.25006 | 6.58100 | 0.13314 | 0.01845 | 0.00012 |

Z-distance of Quad = 3.57798

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43333 | 0.43195 | 0.15693 | 0.16110 | 0.15943 | 0.15946 |
| Upstream End (-Z) | 0.43216 | 0.43308 | 0.16131 | 0.15664 | 0.15981 | 0.15917 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X