LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Thursday, March 20, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000726 / STAMPED – 19 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000726.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00014 | 0.25000 | 3.37132 | 6.81566 | 1.49766 | 0.00011 |
| TB 2 | 0.00012 | 0.25010 | -3.37810 | 6.81057 | 1.50688 | 0.00028 |
| TB 3 | 0.00008 | 0.24999 | -3.38195 | 6.80995 | -1.49430 | 0.00004 |
| TB 4 | 0.00012 | 0.24993 | 3.36724 | 6.81307 | -1.50287 | 0.00013 |
| TB 5 | 0.00011 | 0.25009 | 6.57923 | 0.12973 | 0.00077 | 0.00011 |

Z-distance of Quad = 3.59625

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43481 | 0.43308 | 0.16137 | 0.15891 | 0.16198 | 0.15887 |
| Upstream End (-Z) | 0.43274 | 0.43435 | 0.16028 | 0.16007 | 0.15908 | 0.16104 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X