LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Wednesday, March 12, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000727 / STAMPED – 15 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000727.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00014 | 0.24989 | 3.37264 | 6.81565 | 1.49838 | 0.00006 |
| TB 2 | 0.00014 | 0.24995 | -3.37393 | 6.81289 | 1.50799 | 0.00020 |
| TB 3 | 0.00011 | 0.24997 | -3.37529 | 6.81322 | -1.49266 | 0.00008 |
| TB 4 | 0.00016 | 0.24998 | 3.37145 | 6.81248 | -1.50011 | 0.00019 |
| TB 5 | 0.00011 | 0.25009 | 6.57881 | 0.13793 | -0.00298 | 0.00009 |

Z-distance of Quad = 3.59779

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43499 | 0.43371 | 0.15826 | 0.16072 | 0.16049 | 0.16117 |
| Upstream End (-Z) | 0.43393 | 0.43392 | 0.16014 | 0.16151 | 0.15907 | 0.15987 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

Transformation

- Use TB locations 1, 2, & 3 to establish a Tooling Ball Plane this will be the Spatial Alignment.

- Use TB locations 1 & 2 to establish an axis where the line from TB 2 to TB 1 is the +X direction and will be the Planar Alignment.

- TB 1 will set zero in “X”, “Y”, & “Z”.

| Transformation | X | Y | Z |
| --- | --- | --- | --- |
| Displacement Vector | -85.68165 mm | -173.08666 mm | -38.16225 mm |
| Rotation Matrix | X | Y | Z |
| X | 1.00000 | 0.00041 | -0.00143 |
| Y | -0.00041 | 1.00000 | 0.00011 |
| Z | 0.00143 | -0.00011 | 1.00000 |

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X