LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Tuesday, March 18, 2008 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000728 / STAMPED – 16 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000728.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00013 | 0.25007 | 3.37136 | 6.81500 | 1.50225 | 0.00005 |
| TB 2 | 0.00012 | 0.25001 | -3.37674 | 6.81436 | 1.51240 | 0.00009 |
| TB 3 | 0.00012 | 0.25004 | -3.37757 | 6.81358 | -1.48979 | 0.00009 |
| TB 4 | 0.00011 | 0.24996 | 3.36843 | 6.81394 | -1.49631 | 0.00019 |
| TB 5 | 0.0009 | 0.24995 | 6.58014 | 0.13108 | 0.00958 | 0.00008 |

Z-distance of Quad = 3.59321

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43413 | 0.43324 | 0.16025 | 0.15830 | 0.15840 | 0.16009 |
| Upstream End (-Z) | 0.43347 | 0.43211 | 0.15860 | 0.15840 | 0.15948 | 0.16118 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X