LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Friday, February 29, 2008 (New TB Adapters) |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000737 / STAMPED – 02 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000737.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00025 | 0.25014 | 3.36364 | 6.81310 | 1.47421 | 0.00010 |
| TB 2 | 0.00015 | 0.24993 | -3.37737 | 6.81277 | 1.50489 | 0.00011 |
| TB 3 | 0.00015 | 0.24989 | -3.39121 | 6.81197 | -1.48706 | 0.00012 |
| TB 4 | 0.00018 | 0.24996 | 3.35099 | 6.81233 | -1.51311 | 0.00016 |
| TB 5 | 0.00018 | 0.25013 | 6.57793 | 0.13861 | 0.00884 | 0.00028 |

.

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43307 | 0.43386 | 0.16208 | 0.15863 | 0.16223 | 0.15637 |
| Upstream End (-Z) | 0.43608 | 0.43343 | 0.16074 | 0.16093 | 0.15813 | 0.16024 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

Transformation

- Use TB locations 1, 2, & 3 to establish a Tooling Ball Plane this will be the Spatial Alignment.

- Use TB locations 1 & 2 to establish an axis where the line from TB 2 to TB 1 is the +X direction and will be the Planar Alignment.

- TB 1 will set zero in “X”, “Y”, & “Z”.

| Transformation | X | Y | Z |
| --- | --- | --- | --- |
| Displacement Vector | -85.27366 mm | -173.03849 mm | -37.87992 |
| Rotation Matrix | X | Y | Z |
| X | 0.99999 | 0.00005 | -0.00455 |
| Y | -0.00005 | 1.00000 | -0.00027 |
| Z | 0.00455 | 0.00027 | 0.99999 |

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X