LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Tuesday, March 11, 2008 (New TB Adapters) |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000739 / STAMPED – 06 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000739.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00019 | 0.25005 | 3.37476 | 6.81419 | 1.49338 | 0.00016 |
| TB 2 | 0.00023 | 0.25007 | -3.37134 | 6.81078 | 1.52752 | 0.00010 |
| TB 3 | 0.00022 | 0.24998 | -3.38616 | 6.81159 | -1.46784 | 0.00012 |
| TB 4 | 0.00027 | 0.25006 | 3.36310 | 6.81075 | -1.50127 | 0.00010 |
| TB 5 | 0.00019 | 0.24999 | 6.58495 | 0.15541 | -0.00801 | 0.00035 |

Z-distance of Quad = 3.58411

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43359 | 0.43371 | 0.15681 | 0.16007 | 0.16049 | 0.16117 |
| Upstream End (-Z) | 0.43367 | 0.43335 | 0.15953 | 0.16097 | 0.15733 | 0.16127 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

Transformation

- Use TB locations 1, 2, & 3 to establish a Tooling Ball Plane this will be the Spatial Alignment.

- Use TB locations 1 & 2 to establish an axis where the line from TB 2 to TB 1 is the +X direction and will be the Planar Alignment.

- TB 1 will set zero in “X”, “Y”, & “Z”.

| Transformation | X | Y | Z |
| --- | --- | --- | --- |
| Displacement Vector | -85.61321 mm | -173.04761mm | -38.31821 mm |
| Rotation Matrix | X | Y | Z |
| X | 0.99999 | 0.00051 | -0.00506 |
| Y | -0.00050 | 1.00000 | 0.00027 |
| Z | 0.00506 | -0.00027 | 0.99999 |

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X