LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Thursday, December 06, 2007 |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000739 / STAMPED - 06 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS UNDULATOR QUADS\000739.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on aluminum base plate (that mates to girder).

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00065 | 0.25043 | 3.37932 | 6.31405 | 1.50242 |
| TB 2 | 0.00047 | 0.25069 | -3.37270 | 6.31094 | 1.53354 |
| TB 3 | 0.00050 | 0.25043 | -3.38726 | 6.31163 | -1.46457 |
| TB 4 | 0.00067 | 0.25052 | 3.36642 | 6.31108 | -1.49521 |
| TB 5 | 0.00205 | 0.25126 | 6.26829 | 0.00434 | 0.01615 |

.

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43337 | 0.43377 | 0.15675 | 0.16051 | 0.16095 | 0.16101 |
| Upstream End (-Z) | 0.43341 | 0.43407 | 0.15960 | 0.16031 | 0.15738 | 0.16149 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

Transformation

- Use TB locations 1, 2, & 3 to establish a Tooling Ball Plane this will be the Spatial Alignment.

- Use TB locations 1 & 2 to establish an axis where the line from TB 2 to TB 1 is the +X direction and will be the Planar Alignment.

- TB 1 will set zero in “X”, “Y”, & “Z”.

| Transformation | X | Y | Z |
| --- | --- | --- | --- |
| Displacement Vector | -85.73187 mm | -160.34629 mm | -38.51952 mm |
| Rotation Matrix | X | Y | Z |
| X | 0.99999 | 0.00046 | -0.00461 |
| Y | -0.00046 | 1.00000 | 0.00023 |
| Z | 0.00461 | -0.00023 | 0.99999 |

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X