LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Monday, January 14, 2008 (New TB Adapters) |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000740 / STAMPED – 05 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000740.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00018 | 0.25044 | 3.36946 | 6.81375 | 1.48577 | 0.00023 |
| TB 2 | 0.00024 | 0.25040 | -3.37902 | 6.81186 | 1.47715 | 0.00021 |
| TB 3 | 0.00033 | 0.25041 | -3.37429 | 6.81283 | -1.51989 | 0.00043 |
| TB 4 | 0.00018 | 0.25038 | 3.37708 | 6.81233 | -1.51064 | 0.00023 |
| TB 5 | 0.00026 | 0.25044 | 6.58746 | 0.13314 | -0.00248 | 0.00025 |

.

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43196 | 0.43538 | 0.15902 | 0.15881 | 0.16117 | 0.16044 |
| Upstream End (-Z) | 0.43533 | 0.43288 | 0.16002 | 0.16019 | 0.15572 | 0.16085 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



	milliradians

Transformation

- Use TB locations 1, 2, & 3 to establish a Tooling Ball Plane this will be the Spatial Alignment.

- Use TB locations 1 & 2 to establish an axis where the line from TB 2 to TB 1 is the +X direction and will be the Planar Alignment.

- TB 1 will set zero in “X”, “Y”, & “Z”.

| Transformation | X | Y | Z |
| --- | --- | --- | --- |
| Displacement Vector | -85.68088 | -173.05742 | -37.57325 |
| Rotation Matrix | X | Y | Z |
| X | 1.00000 | 0.00028 | 0.00128 |
| Y | -0.00028 | 1.00000 | -0.00032 |
| Z | -0.00128 | 0.00032 | 1.00000 |

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X