LCLS Undulator Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Scott Anderson |
| Date: | Thursday, January 25, 2008 (New TB Adapters) |
| Work Order/Charge No.: | 88-1400-5 |
| Serial Number: | SLAC – 000741 / STAMPED – 08 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/LCLS UNDULATOR QUADS/000741.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Plane on where Aluminum Base Rests

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Top View looking from +Y

Tooling Ball Adapter Cylinder Projected 1” Offset to the Tooling Ball Adapter Plane

| Tooling Ball | FORM | Cyl. Dia. | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00021 | 0.24997 | 3.38451 | 6.81459 | 1.49326 | 0.00011 |
| TB 2 | 0.00016 | 0.24995 | -3.35849 | 6.81228 | 1.52888 | 0.00017 |
| TB 3 | 0.00013 | 0.24993 | -3.37772 | 6.81208 | -1.46101 | 0.00009 |
| TB 4 | 0.00015 | 0.24989 | 3.36961 | 6.81125 | -1.49888 | 0.00012 |
| TB 5 | 0.00011 | 0.24999 | 6.58344 | 0.15021 | 0.01556 | 0.00031 |

.

Pole Tip Additional Data

*Data looking from Downstream End

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 0.43449 | 0.43423 | 0.15901 | 0.16309 | 0.15935 | 0.15782 |
| Upstream End (-Z) | 0.43522 | 0.43443 | 0.15850 | 0.15981 | 0.16106 | 0.16277 |

Quadrupole Roll Angle

** Tolerance in milliradians is ± 5

Roll of the Base of Quad to Poles



milliradians

Transformation

- Use TB locations 1, 2, & 3 to establish a Tooling Ball Plane this will be the Spatial Alignment.

- Use TB locations 1 & 2 to establish an axis where the line from TB 2 to TB 1 is the +X direction and will be the Planar Alignment.

- TB 1 will set zero in “X”, “Y”, & “Z”.

| Transformation | X | Y | Z |
| --- | --- | --- | --- |
| Displacement Vector | -85.82406 mm | -173.05867 mm | -38.39396 mm |
| Rotation Matrix | X | Y | Z |
| X | 0.99999 | 0.00034 | -0.00528 |
| Y | -0.00034 | 1.00000 | -0.00007 |
| Z | 0.00528 | 0.00007 | 0.99999 |

# Text boxes

+Y

+Z

+Y

+X

+Z

TB 5

+X